# Fundamental principles of dismantling and transport of

# old aircrafts.

An airplane, due to its size and weight can not be moved without a long and appropriate study of its personal characteristics and conditions.

The following  actions are essentials and are common for any airplane:

- complete inventory of its actual state and degree of completeness in written and photos.

- dismantling limited to the main components to avoid dispersion and lost of them and to make the transport easier. ( no dismantling of engine bearers, engine, engine cowlings, propellers when possible; no dismantling of doors, control surfaces, seats, canopies).

- use of the aircraft service manual published by the builder to dismantle and move it properly.

- dismantling of the electrical cables, control cables and tubes by their connections.

- identification of all the parts by card attached to the part in a plastic bag.

- packing in plastic bags of all the nuts, bolts and screws fastened to the concerned part or repositionning immediately on the structure.

- building of supports adapted to the wings and fuselage for the moving and the storage.

- gathering of all the components of an aircraft on one location in the storage area ( no dispersion).

- moving of  components in closed trucks or protected by canvas ( in case of bad weather, although it is to avoided to move historic airplanes when it rains).

- loading and unloading inside buildings.

- to have enough manpower at disposal and of good willingness to produce careful work.